## Slide 1: SERDES DC to Daylight 8/9/2024
Terry Fox, BSEE, Montana State University, 1969
1420 Gilman Blvd NW, Suite2-2128
Issaquah, WA 98027
www.siemc.com
tfox@siemc.com
425 391-8696

## Slide 2: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 3: EM Field Theory .. ie Maxwell’s Equations
D dS = Q = p dv
B dS = 0
E dL =
H dL = I = J dS
vol
s
Surface integral of magnetic flux density is zero …
no magnetic point charge
Closed Line integral of magnetic flux
= current enclosed = surface integral
of current density
Sum of the Electro Static Potential around a closed loop
assuming no changing B field = 0
Closed Surface integral of D
Electric flux density = charge enclosed
= vol integral of volume charge density
D = eo E
B = u0 H
dt
d

## Slide 4: Transmission Line Behavior Signal Current & Return Current
Source
Load
Return Current
Signal Current
Plane is connected to Power or Ground of the DRIVER
End on view
Side View

## Slide 5: SERDES
Vdda
Vssa
Vssb
Vddb
VRef B
Vng
A+
A-
CTLE & DFE EQ
Clock Recovery
Digital Equalization
Data Recovery
Serial to Parallel
Parallel to Serial
Converter +FFE
Serial Input
Serial Output
SERDES is not differential it is complimentary single ended
Parallel
Buss
Input
Parallel
Buss
Output

## Slide 6: Differential Impedance VS Single Ended Impedance
50 ohm single x 99.8 ohm Diff 7 x 20 x 7
6 mils from GND2 & 12 mils from GND5
Electric B Field Blue Magnetic H Field Red
61 ohm single x 99 ohm diff 2.7 x 4 x 2.7 4 mils from GND 2 and 8 mils from GND 5
Electric B Field Blue Magnetic H Field Red

## Slide 7: Transmitter
A+ A- is 750mV to 1.2V ie 450mV hence 900mV PP
Output swing is limited by Vdda-Vssa, Rp and Rg
Vdda 1.2V
Vssa 0V
Forward Feedback Equalization
This is generally De-emphasis based
on prior bits. # Taps simply means
how many bit times are we taking
into account. Theoretically could have
Pre-emphasis also.
If we have a string of 1’s we reduce drive
strength to minimize capacitive over charge
Rp ~ 50Ohms
Rg ~ 50 ohms
A+
A-

## Slide 8: Receiver
RX
Vddb
Serial Out
CTLE
Continuous Time Linear Equalization
filter / amplifier in front of comparator
Clock Recovery
Data Recovery
DFE
What is the sensitivity
and hysteresis of comparator?
Decision Feedback Equalization

## Slide 9: Loss Margin
Vdda-Vssa | TX Peak to Peak Voltage | RX Sensitivity |  | Difference in db
1200mV | 800mV | 100mV |  | -18db
1200mV | 800mV | 50mV |  | -24db
1000mV | 600mV | 50mV |  | -21db
FFE | CTLE | DFE |  | 
9db max | 9db max | 9db max |  | ???????
High volume design choices are driven by reducing per unit manufacturing cost.
Minimal loss margins require highly accurate design validation  High Engineering Cost
Low volume design choices are driven by reducing engineering cost.
Minimizing design time requires greater design and manufacturing loss safety margins.
The trade off is more money in the board and less money in the engineering.

## Slide 10: Engineering cost vs Manufacturing cost
What is the maximum reasonable loss margin for this technology?
What will it take to design a successful product within that constraint?
Minimum per unit manufacturing cost  tight design margins.
Precise characterization of the elements of the design are required to achieve success with tight margins.
Precise characterization will require more engineering to get answers accurate enough to assure success.
Minimum engineering requires larger design margins to assure success.

## Slide 11: Validation Methods
IBIS-AMI Simulation … up to 25Gbps … NRZ … eye diagram
  Requires getting model for Driver & Receiver from chip manufacturer
  Requires model of PCB stack-up for Er, Df, dimensions, etc
  Requires simulator with lossy line trace simulation
  Requires 3D FEM Touchstone ( S-parameter) models for vias & caps
  Requires 3D FEM Touchstone ( S-parameter) models connectors
COM Simulation … above 25Gbps…PAM4…graphs vs spec
  Requires everything IBIS-AMI requires except Driver/Receiver model from manufacturer
  Requires industry standard specifications for interconnect
Build & Pray  Going out of business plan

## Slide 12: Design and Manufacturing Safety Margin
A successful design must have a manufacturing yield of 98% or better.
A successful design must allow for engineering uncertainty.
A 3db D&M Safety Margin is the minimum I will accept.
A 6db D&M safety margin will drastically reduce the engineering effort necessary to assure product success.

## Slide 13: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 14: Trace Loss
Trace loss numbers come from a well documented stack-up  great simulator
  Z-Planner or HyperLynx Stack-up editor
12 inches, 4, 8, 4 FR4, 16GHz, loss = 15.8db
12 inches 7, 20, 7 FR4 16GHz, loss = 17.4bd
12 inches, 4, 4, 4 Meg 6, 15GHz, loss = 9.8
12 inches 7, 20, 7 Meg 6 16GHz, loss = 7.8db

## Slide 15: Trace Loss vs Board Space
Key point….loss for given stack-up is also affected by trace width & spacing
Lower loss requires more board routing space
12 inches 7, 20, 7 FR4 16GHz, loss = 7.8db
12 inches, 3.5, 6, 3.5 FR4, 16GHz, loss = 18db

## Slide 16: Trace Loss Meg 6 vs FR4
12 inches 7, 20, 7 Meg 6 16GHz, loss = 7.8db
12 inches, 3.5, 6, 3.5 MEG 6, 16GHz, loss = 10.5db
12 inches, 3.5, 6, 3.5 FR4, 16GHz, loss = 18db
12 inches 7, 20, 7 FR4 16GHz, loss = 7.8db

## Slide 17: Demo Hyperlynx Stack-up Editor or Z-Planner

## Slide 18: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 19: Equalization
Feed Forward Equalization
  Reduced drive strength if 1’s or 0’s were repeated. This minimized the excess charge in the receiver that must be overcome by the next change of input voltage using NRZ signaling.
Continuous Time Linear Equalization
  Receiver amplified higher frequencies and reduced lower frequencies.
Decision Feedback Equalization
  Adds or subtracts voltage at comparator based on past bit pattern. This primarily aids with minimizing the effect of reflections.

## Slide 20: Simple TX line VS EQ
No EQ 0.435 x 0.0957
DFE only 0.721 x 0.279
CTLE only 0.706 x 0.275
FFE only 0.740 x 0.271
CTLE & DFE 0.762 x 0.296
EQ results in about 9.8db of improvement

## Slide 21: Same Channel without discontinuity

## Slide 22: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 23: Skew
Skew Demo

## Slide 24: SKEW
UI = 33.33ps
SKEW = 7.331pS or 2.2%

## Slide 25: SKEW
UI = 33.33ps
SKEW = 14.66pS or 4.3%

## Slide 26: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 27: Jitter
No Jitter
1% UI Gaussian

## Slide 28: Jitter
No Jitter
2% UI Gaussian

## Slide 29: Jitter
No Jitter
3% UI Gaussian

## Slide 30: Jitter
No Jitter
4% UI Gaussian

## Slide 31: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 32: CrossTalk
3” Top 30GB/s
3” Top, 8,8,8
30GB/s
loss 5.6db

## Slide 33: CrossTalk
3” Top 30GB/s
3” Top, 8,30,8
30GB/s
Loss 4.18db

## Slide 34: CrossTalk
3” Top 8,8,8 30GB/s
2 “h”
“h”= 4 mils
3” Top, 8,30,8
30GB/s
7.5 “h”
V^ 1.43db
T^ 0.83 bd
=20 log V1/V2

## Slide 35: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 36: Connector.s4p

## Slide 37: Connectors
Best case is to get S-parameter (Touchstone) model from connector manufacturer
If not available, fake it by calling it a via with a funny layer spacing

## Slide 38: Samtec 48 pin board to board connector

## Slide 39: SAMTEC AMxD GGSS

## Slide 40: SAMTEC AMxD GSSG

## Slide 41: Samtec GSSD
RL 8db  35GHz IL 3.2db  35GHz

## Slide 44: TFox Dog Patch Flats method if no connector manufacturer data available
Make the connector look line a via with a funny board stack-up

## Slide 47: Connector 100 mil x 100mil x 2 stitch V199_19.sp4

## Slide 48: Small close

## Slide 49: 100 Space

## Slide 50: 25mil

## Slide 51: 25mil

## Slide 52: 25mil

## Slide 53: 50 Space

## Slide 54: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 55: Blocking Capacitors based on footprint @ 26 Gbps
No capacitor simple 7mil trace
  0.687UI x 0.237V
402 16 mils x 8 mils
  0.687UI x 0.232
201 8mils x 4 mils
  0.673UI x 0.226V
603 24mils x 12 mils
  0.685UI x 0.227V
  Does not account for added height above ground plane
402 = 16 mils x 8 mils
201 = 8 mils x 4 mils
603 = 24 mils x 12 mils

## Slide 56: Blocking Capacitors footprint Capacitance issue 30Gbps
Open Channel 7mil traces
402 16 mils x 8 mils
201 8mils x 4 mils
603 24mils x 12 mils
402 = 16 mils x 8 mils
201 = 8 mils x 4 mils
603 = 24 mils x 12 mils

## Slide 57: Blocking Capacitors footprint Capacitance issue 34Gbps
Channel 7mil traces No FFE
Open Channel 7mil traces
FFE Optimized at TX
402 18mils x 8 mils +FFE
402 18mils x 8 mils NO FFE
402 = 16 mils x 8 mils
201 = 8 mils x 4 mils
603 = 24 mils x 12 mils

## Slide 58: Blocking Capacitors footprint Capacitance issue 56B/s, Reduced Length 4” to reduce loss
Channel 7mil traces 402 18mils x 8 mils No FFE
Channel 7mil traces 402 18mils x 8 mils FFE Optimized at TX
Channel 7mil traces 603 24mils x 12 mils FFE Optimized at TX
402 = 16 mils x 8 mils
201 = 8 mils x 4 mils
603 = 24 mils x 12 mils

## Slide 59: Blocking Capacitors
Moral of Story…
  Attenuation is KING!!!
  Equalization is Queen!!!
  Blocking Cap is just a blocking Cap, use what works
  Better to use cap with footprint same width as trace or close
  Cap needs to have enough capacitance to pass low frequencies
  Be careful of some super high capacitance devices because some have very high ESL
https://ksim3.kemet.com/capacitor-simulation

## Slide 60: Blocking Capacitors
https://www.murata.com/enus/products/productdetail?partno=GRM022R60J332KE19%23
15.7 mils x 7.8 mils

## Slide 61: Blocking Capacitors
https://www.murata.com/products/productdetail.aspx?partno=GRM011R60G332KE01%23
9.8mil x 4.9mil

## Slide 62: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 63: Viva la Vias
The key to a happy life with vias is to understand 2 key issues.
1. How does the return current flow?
2. Are there any stubs that approach ¼ lambda of the highest frequency of interest in the design?

## Slide 64: Perfect VIA
Layer 1 to Layer 3, Ground in Middle, separation 30mils, 10mil drill, 20 mil pad, back drilled to layer 4, Common anti pad, no stitching vias, 50MHz to 30GHz @ 26GHz IL1.5db RL 18bd
V9_03

## Slide 65: OK VIA
Layer 1 to Layer 3 Ground in Middle separation 75mils 10mil drill, 20 mil pad, back drilled to layer 4, Common anti pad, no stitching vias, 50MHz to 30GHz @ 26GHz IL1.9db RL 12bd
V9_75

## Slide 66: Top to Bottom VIA
Layer 3 to Layer 12 separation 30mils 10mil drill, 20 mil pad,, Common anti pad, 4 stitching vias, 50MHz to 30GHz @ 26GHz IL1.9db RL 9.2db
V5_30

## Slide 67: L3 to L12 VIA
Layer 3 to Layer 12 separation 75mils 10mil drill, 20 mil pad,, Common anti pad, 4 stitching vias, 50MHz to 30GHz @ 26GHz IL1.9db RL 9.2db
V5_30

## Slide 68: Drill Spacing Comparison
Layer 3 to Layer 12 separation 75mils 10mil drill, 20 mil pad,, Common anti pad, 4 stitching vias, 50MHz to 30GHz @ 26GHz IL1.9db RL 9.2db
V5_30
Yellow RL close
Green IL Close
Red RL wide
Blue IL wide

## Slide 69: More on Vias
Vias connect the signal from one routing layer to another routing layer.
SERDES vias have two signal vias and generally two stitching vias to provide a low impedance return current path in the immediate vicinity of the signal via.
Critical factors are Insertion Loss and Return Loss
…… and the smoothness of those curves
NO! The return current for P signal DOES NOT flow on the N signal. Remember this is LVDS not true differential with a transformer.

## Slide 70: More on Vias
Highly accurate detailed via insertion loss and return loss values are only true for the SPECIFIC via transition within a SPECIFIC stack-up with a SPECIFIC Er and Df for a SPECIFIC layer pair transition.
Get a clue…open an Excel spread sheet right now and start building a library of via configurations and the performance of each configuration.

## Slide 71: More onVias
Stack-up | Layer Pair | Sig Via Spacing | Stitch Via | Drill Size | Back Drill | Results File
12L4mSG | 1/3 | 30 | none | 10/20 | BD | V1-09
12L6mSG | 1/3 | 75 | none | 10/20 | No BD | V9
12L6mSG | 3/Bot | 75 | 4@min | 8/18 | None | V5
12L6mSG | 3/Bot | 75 | 4@min | 10/20 | None | V1_15
12L2SG | 3/Bot | 30 C | 4@min | 10/20 | None | V1_16
12L6mSG | 3/4 | 30 | 4@min | 10/20 | B-Gnd5 | V9_05
12L6mSG | 1/3 | 30 C | None | 10/20 | B-Gnd5 | V1_14
12L6mSG | 1/3 | 40 C | None | 10/20 | B-Gnd5 | V1-13
12L6mSG | 1/3 | 75 C | None | 10/20 | B-Gnd5 | V1_11
RL -17bd, IL 0.42db
RL -15.3, IL 0.442
RL -12.7, IL 0.64
RL -14.5, IL 0.657
RL -15, IL 0.597
RL-14.4 IL 0.32
RL -6 IL 4.0db
RL -18 IL 0.37
RL -20 IL 0.4

## Slide 72: Via V1_09
V1_09 10-20 75 mil BD Gnd5

## Slide 73: Via V1_09 0.4db IL -20db RL
V1_09 10-20 75 mil BD Gnd5

## Slide 74: V1-10 30mil space

## Slide 75: V1-10 30mil space
30mil space BD Gnd-5 No Stitching vias, 0.425db IL -17db RL

## Slide 76: Viva la Vias
Left is 12 layers with 6mils signal to ground
Right is 12 layers with 4mils signal to ground
12L4mSG
12L6mSG

## Slide 77: Via Lab
Lab exercise
Create a via from Bot (L12 ) to Layer 3
Find a configuration that gives an insertion loss of less than 1db and a return loss lower than -15db
Create a via from Top to L3.
Create a via that gives an insertion loss less than 0.6db and a return loss lower than -15db.

## Slide 79: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 80: NRZ vs PAM-4
NRZ (PAM-2)
  has 1 comparison point
  S/N is PP Signal / PP Noise
PAM-4
  has 3 comparison points
  S/N is 1/3 PP Signal / PP Noise
  Standard for 26Gbps and higher
PAM-4 IS NOT a free lunch

## Slide 81: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 82: The Challenge
Design a two-board system that runs at 26GB/s with a total distance of 12” including a connector and a DC blocking capacitor.

## Slide 83: The Challenge
Total distance from TX to RX is 12” with the connector roughly in the middle. Daughter card has the connector on the bottom and the BGA & DC Blocking Capacitor on the top. Assume, for several reasons, the bulk of the routing must be done on interior routing layers.
Use driver and receiver from Mentor Generic_SERDES Lib
Use a 12-layer board with 4 center planes for power. G sP sP G
Use Connector.sp4…not a great connector, but that is all I had
A valid eye is defined as 50% of UI and 100mV height
26 GB/s is data rate
DO NOT use FFE, CTLE, or DFE until you have a legal eye without equalization

## Slide 84: The Challenge
Detailed view of driver side
J1 is the connector.sp4
TL39 & TL40 is simple ( perfect ) fan-out

## Slide 85: The Challenge
Detailed view of receiver side.
TL45-TL50 is a 1st level model for the DC blocking capacitor
TL51-TL52 are the fan-in to the receiver. Assume the connections to the BGA’s are perfect.

## Slide 86: The Challenge
Total budget for maximum signal loss is -18db
  20Log( 100mV / 800mV pp) = -18db maximum loss in technology
Initial Loss Budget
  12” transmission line 9db
  Everything else 9db

## Slide 87: The Challenge
Budget Guestimates
  Routing Loss = 9db
  6ea Top to Routing Layer 3 vias at 0.5db each = 3db
  1ea Bottom to Routing Layer 3 via = 1db
  1ea connector = 2.5db
  DC Blocking Capacitor = 1.5db
  Remaining design margin assuming no reflections
  18db -17db = 1db safety margin
  If I can not beat these estimates, we need to change the requirements. A 3db safety margin is the smallest reasonable margin I will sign off on.

## Slide 88: The Challenge
First level sanity check.
  What combination of laminate, stack-up, and signal width-space can achieve a loss of less than 9db
  FR4 has a loss tangent ( Df ) of 0.02. Can FR4 possibly work? NO!!!
  Meg6 has a loss tangent ( Df ) of about 0.004. Can this work? Maybe?
  If Meg6 cannot work, go back and change the dimensions of the problem.
  However, Meg6 can achieve a total loss of under 9db with the correct stack-up and routing rules.

## Slide 89: The Challenge
Second level sanity check..Vias!
  Routing layer 3 is the closest to the Top where the BGA and DC blocking capacitor are mounted. Therefore layer 3 will be my primary routing layer.
  We need a minimum of 6 Top-Routing Layer 3 vias
  The connector to the Mother Board is on Top but the connector to the Daughter Card is on the Bottom.
  Hence, we need 1ea via from Bottom to Routing Layer 3.
  We might need a cross over. The choices are internal 3 to 4 or uses two more Top-Layer 3 vias and cross on the Top layer.

## Slide 90: The Challenge
Develop a Top-Layer 3 via that has insertion loss of less than 0.5db and return loss of less than -18db at 13GHz. A perfect design will require of 6ea of this class of via consuming 3db of our design margin
Develop a Bottom-Layer 3 via. If only one is required, we can allow up to 1db for this via as long as the return loss does not get out of hand.
Keep RL for all vias below 10db and preferably below 15db
Develop a Routing Layer 3 to Routing Layer 4 via to use as a cross over if needed.

## Slide 91: The Challenge
Third level sanity check ...DC Blocking Capacitor
  The DC Blocking Capacitor is used to protect the connected cards from DC offset power issues.
  We will assume a minimum pass band frequency of 50MHz for the data signal.
  DC blocking capacitor should be very low loss. An equivalent impedance of 2 ohms or less will probably make no difference in a reasonable design. The primary issue with blocking capacitors is the Return Loss due to the physical size of the device.
  Since size matters, we will look for the smallest package that will pass 50MHz with less than 2ohms equivalent impedance.
  To handle the Return Loss issue for a first level simulation we will use a transmission line on the surface with dimensions equivalent to the mounting pads of the capacitor spaced according to the minimum manufacturing rules.

## Slide 92: The Challenge
Put it all together and see if it works wo EQ.

## Slide 93: The Challenge
Put it all together and see if it works with CTLE

## Slide 94: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 95: Addendum to Challenge
The following slides add more detail to getting the needed answers to complete the challenge

## Slide 96: Stack-up and Routing Sanity Checks
12” trace FR4 Df = 0.02 on Route Layer 3 is > 17db

## Slide 97: Stack-up and Routing Sanity Checks
12” 4mil wide trace Meg6 Df = 0.004 on Route Layer 3 is < 9db

## Slide 98: Stack-up and Routing Sanity Checks
12” 7mil trace 20mil space Meg6 Df = 0.004 on Route Layer 3 is < 7db

## Slide 99: Via Sanity check
Winning Top-Route3 via, 0.6db Loss & < -18db Return Loss

## Slide 100: Via Sanity check
Winning Top-Route3 via, 0.6db Loss & < -18db Return Loss

## Slide 101: Via Sanity check
Winning Bottom to Route 3 via 0.6db loss -15db Return Loss

## Slide 102: Connector
At 13GHz
Insertion Loss -2.5db
Return Loss -12db

## Slide 104: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 105: SERDES DC to Daylight Process 8/9/2024
Terry Fox, BSEE, Montana State University, 1969
1420 Gilman Blvd NW, Suite2-2128
Issaquah, WA 98027
www.siemc.com
tfox@siemc.com
425 391-8696

## Slide 106: SERDES Design Process
Initial Analysis
Detail Design
Pre-Layout Design Review
Layout
Final Validation of all SERDES circuits as routed
Validate Power Delivery Network as routed
Pre-Fabrication Design Review
Fabricate
Verify Safety Margin through lab tests
Post Fabrication Design Review

## Slide 107: SERDES Design Process
Initial Analysis
Detail Design
Pre-Layout Design Review
Layout
Final verification of all SERDES circuits
Validate Power Delivery Network design as routed
Pre-Fabrication Design Review
Fabricate
Verify Safety Margin through lab tests
Post Fabrication Design Review

## Slide 108: Process
Initial Analysis
  Is there any conceivable combination of elements that will allow this design to work with a descent safety margin?
  No. Change the Requirements
  Yes. Get a detailed quotation from a board fabricator.

## Slide 109: SERDES Design Process
Initial Analysis
Detail Design
Pre-Layout Design Review
Layout
Final Validation of all SERDES circuits as routed
Validate Power Delivery Design as routed
Pre-Fabrication Design Review
Fabricate
Verify Safety Margin through lab tests
Post Fabrication Design Review

## Slide 110: SERDES Design Process
Detail Design
  Based on REAL board stack-up and performance data from at least one REAL board vendor.
  Perform simulations on each class of SERDES circuit to establish routing guide-lines
  Trace width & spacing on a per layer basis
  Precise via construction for each type of transition
  Max length
  Max skew
  Max skew between certain elements
  Trombone rules
  Embedded capacitance split power plane rules

## Slide 111: SERDES Design Process
Initial Analysis
Detail Design
Pre-Layout Design Review
Layout
Final Validation of all SERDES circuits as routed
Validate Power
Pre-Fabrication Design Review
Fabricate
Verify Safety Margin through lab tests
Post Fabrication Design Review

## Slide 112: SERDES Design Process
Pre-Layout Design Review
  EE, Layout Designer, devil’s advocate
  Purpose is to document all layout rules and explain the reason behind the rules to the layout designer.
  Give all parties involved with the design a chance to ask questions, make suggestions, and raise objections.
  DO NOT do anything more than initial floor planning until everyone agrees to the layout design rules.
  Once everyone understands the plan and agrees, proceed to Layout

## Slide 113: SERDES Design Process
Initial Analysis
Detail Design
Pre-Layout Design Review
Layout
Final Validation of all SERDES circuits
Validate Power
Pre-Fabrication Design Review
Fabricate
Verify Safety Margin through lab tests
Post Fabrication Design Review

## Slide 114: SERDES Design Process
Layout
  Floor Plan
  Route one example of each type SERDES circuit for export to simulation to validate the actual layout performance
  If there are multiple topologies, one example of each SERDES topology must be exported and validated in simulation.
  Export SERDES routes and validate routing progress on the fly to identify any issues as early as possible. Mid layout simulations can identify critical trade-off issues.

## Slide 115: SERDES Design Process
Initial Analysis
Detail Design
Pre-Layout Design Review
Layout
Final Validation of all SERDES circuits
Validate Power Delivery Network design
Pre-Fabrication Design Review
Fabricate
Verify Safety Margin through lab tests
Post Fabrication Design Review

## Slide 116: SERDES Design Process
Final validation of all SERDES circuits
  Use automated tools to rigorously validate all SERDES routes for design safety margin and identify outliers.
  Questionable routes must be analyzed on a 3D FEM basis to get a more precise understanding of the circuit performance.
  Power delivery performance must be validated

## Slide 117: SERDES Design Process
Initial Analysis
Detail Design
Pre-Layout Design Review
Layout
Final verification of all SERDES circuits
Validate Power
Pre-Fabrication Design Review
Fabricate
Verify Safety Margin through lab tests
Post Fabrication Design Review

## Slide 118: SERDES Design Process
Validate Power Delivery Network design
  Power Delivery Network topology
    Common errors
  Power plane noise
  DC drop

## Slide 119: SERDES Design Process
Initial Analysis
Detail Design
Pre-Layout Design Review
Layout
Final verification of all SERDES circuits
Validate Power Delivery Network design
Pre-Fabrication Design Review
Fabricate
Verify Safety Margin through lab tests
Post Fabrication Design Review

## Slide 120: SERDES Design Process
Pre-Fabrication Design Review
  EE, Layout Designer, Mfg Rep., devils advocate
  Did you cover the bases?
  Should this board be fabricated at this point?
  What is predicted design safety margin?
  If less than 3db, you are just gambling.
Fabricate board
Test Prototype Board’s performance and get a rough indication of safety margin
  If satisfactory, release to production
  If not satisfactory…..fix your process!
Post Fabrication Design Review….if necessary

## Slide 121: SERDES Design Process
Initial Analysis
Detail Design
Pre-Layout Design Review
Layout
Final verification of all SERDES circuits
Verify Power
Pre-Fabrication Design Review
Fabricate
Verify Safety Margin through lab tests
Post Fabrication Design Review

## Slide 122: Pre-Layout Analysis and Design
    The purpose is to discover and validate a layout strategy that will produce the electrical performance required or provide evidence that the design cannot be built as conceived.
    Assuming a modern 26Gbps NRZ technology my initial trace budget would be about 12db
    What combination of laminate type, layer stack-up, and routing space - trace width will go 12” at 13GHz with less than 12db of attenuation
    In the total loss margin is with gross simulation that are fast and easy to establish a base line for laminate material, layer stack-up refine down to more detailed simulations as long as the easy simulations.
    At the first level we simulate stack-up, laminate types, and routing rules that will enable a minimum drive level signal to arrive at the receiver with no more than 12db of loss at the Nyquist frequency. If a layout strategy appears valid, we will refine the performance estimate until the predicted performance including a design margin meets the requirements recursively simulate with higher fidelity models until we can prove the strategy will not work or we prove it will work and also result in an adequate sasuch time as the predicted performance plus and simulation uncertainty will meet the performance requirements requires simulation with ever more accurate models until we can be confident that the predicted performance including any simulation uncertainty will result in a working system

## Slide 123: Layout Phase
Floor Plan
Place the major components and route at least one SERDES channel.
Export partial design to simulation system and verify the performance of the routed channel.
If the safety margin is marginal, change something to improve it.
When all SERDES channels have been routed, re-simulate all channels to validate their performance including channel to channel cross talk.
If all the channels have an adequate safety margin and there are no weird outliers, perform the Post Layout, Pre-Fabrication Design Review and release to design fabrication.

## Slide 124: Post Layout / Pre Fabrication Phase
Re-simulate all high-speed traces using layout “AS BUILT” data
Check PDN’s
Gather all relevant players and perform a Post Layout / Pre Fab Review

## Slide 125: Post-Fabrication Design Review
If the system meets its performance requirements in the lab tests, move on to production.
If the design does not meet the performance requirements in the lab, re-examine the assumptions, methods, or review process to identify the error and modify the process.
  Any method used to predict the electrical performance of mechanical structures and silicon devices will have accuracy limits.
  Early cycle circuit design performance simulations will be based on data sheets and 2D simulation models. 2D simulation models are fast and easy but have greater uncertainty than a full 3D EM model.
  Late cycle design performance simulations will be a mix of data sheets, 2D, and 3D models. 3D models require more time but produce models with more precise fidelity.
  Data sheet models either come from the part manufacturer or are measured in the lab, de-embedded, and incorporated into the total circuit simulation as a Touchstone or S-Parameter model.

## Slide 126: How much analysis is necessary before fabricating a prototype?
  When the predicted design performance meets all requirements plus a reasonable safety margin, fabricate the design.
  If the simulation error limits are within the safety margin, the prototype will work
  Low volume products generally benefit from investing insurance money in each production board in order to assure required performance in the minimum design time.
  High-volume products need to achieve the lowest reasonable manufacturing cost. That requires a much thinner design safety margin much more precise refinement of small design layout details. The analysis time and simulation accuracy required in this environment requires significantly more time to arrive at the optimum solution. That means massively more engineering time.
  You can do higher per unit cost and fast or you can do low per unit cost. It is extremely difficult to do both at the same time.
  We need a safe answer in the shortest amount of time.
  If you adopt my method of thinking about the problem and design with a safety margin, you will avoid late cycle performance issues which cause delivery delays and unplanned desperation board spins.

## Slide 127: How much analysis is necessary before building a prototype?
  High-volume products need to achieve the lowest reasonable manufacturing cost.
  Lower manufacturing cost requires much more precise refinement of small design layout details.
  The analysis time and simulation accuracy required in this environment requires a significantly greater effort that using a more expensive per unit solution.
  You can do higher per unit cost and faster design, or you can do lower per unit cost. It is extremely difficult to do both at the same time.

## Slide 128: When is it Good enough to ship?
  The process explained in this class is a recursive refinement of the simulation accuracy.
  The trade off is manufacturing cost vs safety margin vs engineering time.
  Turn the crank until you are satisfied with the results, but do not proceed past a design review until you have the answers necessary and a solid plan to succeed.
  If you adopt my method of thinking about the problem and design with a safety margin, you will avoid late cycle performance issues which cause delivery delays and unplanned desperation board spins.

## Slide 129: SERDES DC to Daylight End Process 8/11/2024
Terry Fox, BSEE, Montana State University, 1969
1420 Gilman Blvd NW, Suite2-2128
Issaquah, WA 98027
www.siemc.com
tfox@siemc.com
425 391-8696

## Slide 130: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 131: COM / JCOM
COM is set of industry standards for validating SERDES connections.
  Ethernet…example…100GBASE-KR4
  Fiber
  HDMI
  JESD
  MIPI D PHY
  OIF-CEI… example…CEI-28G-VSR
  PCIe … …PCIE5.0-32Gts
  USB 3.1… …USB3.1-5G
Assumes minimum specifications for Driver and Receiver
Runs orders of magnitude faster than IBIS-AMI because it is statistical in nature

## Slide 132: COM / JCOM
Informative: Supplementary compliance based information
  FFE - Case 1
  FFE - Case 2
  CTLE - Case 1
  CTLE - Case 2
  DFE Taps Relative to h0 - Case 1
  DFE Taps Relative to h0 - Case 2
  DFE Taps Abs value [V] - Case 1
  DFE Taps Abs value [V] - Case 2
  Intermediate Results - Case 1
  Intermediate Results - Case 2
Informative: Supplementary Links
  Optimized Reference CTLE Transfer Function

## Slide 133: COM / JCOM
CDF plots - Case 2
  CDF with ISI Case 2; CDF with ISI and DD jitter Case 2; CDF with ISI, DD jitter and Xtalk Case 2; CDF with ISI, DD jitter, Xtalk and noise Case 2
ERL plots (PMF)
  PMF of ERL11; PMF of ERL22
ERL plots (CDF)
  CDF of ERL11; CDF of ERL22
Vertical cross-section - Case 1
  Vertical cross-section of the eye Case 1
Vertical cross-section - Case 2
  Vertical cross-section of the eye Case 2
Horizontal cross-section - Case 1
  Horizontal cross-section of the eye Case 1
Horizontal cross-section - Case 2
  Horizontal cross-section of the eye Case 2
Parameters
  ICN (Integrated Crosstalk Noise) - Case 1
  ICN (Integrated Crosstalk Noise) - Case 2

## Slide 134: COM / JCOM
Eye Density / BER Links
  Eye Density / BER Links
Freq. Domain Links
  Channel Freq. Domain Characteristics
  Differential Package and PCB models
  Differential Channel with Package/PCB added
  Voltage Transfer Function (differential channel with packages/PCBs, terminations, Tx transition and Rx noise filters)
  ERL Frequency Domain Response
Time Domain Links
  Time Domain Responses
  ERL Time Domain Links
  PMF with ISI Case 2; PMF with ISI and DD jitter Case 2; PMF with ISI, DD jitter and Xtalk Case 2; PMF with ISI, DD jitter, Xtalk and noise Case 2

## Slide 135: COM / JCOM
Time Domain Links
  Time Domain Responses
  ERL Time Domain Links
Jitter PDF
  All jitter PDF
PDF plots - Case 1
  PMF with ISI Case 1; PMF with ISI and DD jitter Case 1; PMF with ISI, DD jitter and Xtalk Case 1; PMF with ISI, DD jitter, Xtalk and noise Case 1
PDF plots - Case 2
  PMF with ISI Case 2; PMF with ISI and DD jitter Case 2; PMF with ISI, DD jitter and Xtalk Case 2; PMF with ISI, DD jitter, Xtalk and noise Case 2

## Slide 136: Dip at 1.97 nS is connector next 2 are vias, last one is capacitor

## Slide 137: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide

## Slide 138: Design Rule Check tool

## Slide 139: Agenda
How does SERDES work?
Loss Margin
Trace Loss
Equalization
Skew
Jitter
Cross Talk
Connectors
Blocking Capacitors
Vias
PAM-4 vs NRZ
The Challenge
The Challenge Addendum
Design Process
Role of Batch Solutions
  COM / JCOM
  DRC
Exotic Solutions
  Signal Repeaters
  Coax / Twinax
  Optical
  Flexible wave guide